## Slide 1: Lecture-8.1 8086 Microprocessor Interrupt

## Slide 2: What is an interrupt?
capability to suspend the execution of running program and execution of another program to fulfill specific requirement upon request
after finishing the second program, automatically return to the first program and start execution from where it was left

## Slide 3: Why interrupt capability is necessary?
To understand this we will have to review how µP/µC communicate with the outside world.

## Slide 4: Basic block diagram of a µC
µP
MEMORY
I/O
DEVICES
BUS

## Slide 5: First type of communication DEDICATED
µP
I/O
DEVICE 1
BUS
Single I/O device

## Slide 6: Second type of communication POLLED I/O or PROGRAMMED I/O
Disadvantage
  not fast enough
  waste too much microprocessor time
µP
I/O
device1
I/O
device n
BUS
...
You?
You?
You?

## Slide 7: 3RD Type of communication INTERRUPTED I/O
INT
µP
INT
I/O
device1
I/O
device n
BUS
...
INT
INT
INT
Interrupts are particularly useful when I/O devices are slow

## Slide 8
Most microprocessors allow normal program execution to be interrupted by some external signal or by a special instruction in the program.
In response to an interrupt, the microprocessor stops executing its current program and calls a procedure which “services” the interrupt.
A special instruction --- IRET --- at the end of interrupt-service procedure returns execution to the interrupted main program.

## Slide 9
An 8086 interrupt can come from any of the three sources:
  An external signal applied to NMI (Non-Maskable Interrupt) or INTR pin.
    known as hardware interruption
  execution of interrupt instruction INT.
    referred as software interruption
  some error condition produced by execution of an instruction, e.g., trying to divide some number by zero.

## Slide 10
8086 interrupts can be classified into two types:
1) Predefined interrupt
some error condition produced by execution of an instruction, e.g., trying to divide some number by zero.
2) User defined interrupt
  i) hardware interrupt
      An external signal applied to INTR pin
  ii) software interrupt
      execution of interrupt instruction INT

## Slide 11
At the end of each instruction cycle, 8086 checks to see if any interrupts have been requested.
If yes, then 8086 responds to the interrupt by stepping through the following series of major actions:

## Slide 12
It decremented SP by 2 and pushes Flag register on the stack.
It disables 8086 INTR input by clearing IF flag in Flag register
It resets the TF (trap) flag in Flag register
It decremented SP again by 2 and pushes current CS contents on the stack.
It decremented SP again by 2 and pushes current IP contents on the stack.
It does an indirect far jump to the start of the procedure written to respond to the interrupt.

## Slide 13
1. Push FLAGS
2. Clear IF
3. Clear TF
4. Push CS
5. Push IP
6. Fetch ISR
address
main
Program
Interrupt Service Routine (ISR)
PUSH registers
...
...
...
....
...
....
...
....
POP registers
IRET
POP IP
POP CS
POP FLAGS

## Slide 14
How does 8086 get to Interrupt Service Routine?
  Simple. It loads its CS and IP registers with the address of ISR.
  So, the next instruction to be executed is the first instruction of ISR

## Slide 15
How does 8086 get the address of Interrupt Service Routine (ISR)?
  It goes to specified memory location to fetch four consecutive bytes
    higher two bytes to be used as CS
    lower two bytes to be used as IP

## Slide 16
How does 8086 get the address of that specified memory location?
  In an 8086 system, the first 1Kbytes of memory, from 00000 to 003FF, is set aside as a Table for storing the starting addresses of interrupt service routines.
  Since 4 bytes are required to store CS and IP values for each ISR, the Table can hold the starting addresses for up to 256 ISRs.

## Slide 17
The starting address of an ISR is often called
  the interrupt vector or
  the interrupt pointer.
So the Table is referred to as
  interrupt-vector table or
  interrupt-pointer table.

## Slide 18
Next slide shows how the 256 interrupt vectors are arranged in the table in memory
Note that
  the IP value is put in as the low word of the vector
  CS as high word of the vector
Each double word interrupt vector is identified by a number from 0 to 255
INTEL calls this number the TYPE of the interrupt

## Slide 19
AVAILABLE |  | 3FFH |  | TYPE 255 | 
FOR USER |  |  |  | ... | 
(224) |  | 080H |  | TYPE 32 | 
 |  |  |  | TYPE 31 | 
RESERVED (27) |  |  |  | ... | 
 |  | 014H |  | TYPE 5 | 
 |  |  |  | TYPE 4 | 
 |  | 010H |  | INTO OVERFLOW | 
 |  |  |  | TYPE 3 | 
Predefined/ |  | 00CH |  | INT | 
Dedicated/Internal |  |  |  | TYPE 2 | 
Interrupts Pointers |  | 008H |  | NON-MASKABLE | 
(5) |  |  |  | TYPE 1 | 
 |  | 004H |  | SINGLE STEP | 
CS Base Address |  |  |  | TYPE 0 | 
IP Offset |  | 000H |  | DIVIDE ERROR | 

## Slide 20
How does 8086 get the address of a particular ISR?
  In an 8086 system, each “interrupter” has an id#
  8086 treat this id# as interruption type#
  after receiving INTR signal, 8086 sends an INTA signal
  after receiving INTA signal, interrupter releases it’s id#, i.e., type# of the interruption.

## Slide 21: contd...
8086 multiplies this id# or type# by 4 to produced the desired address in the vector table
8086 reads 4 bytes of memory starting from this address to get the starting address of ISR
lower 2 byte is loaded in to IP
higher 2 bytes to CS

## Slide 22: What happens if two or more interrupts occur at the same time?
higher priority interrupts will be served first

## Slide 23: Priorities of 8086 interrupts
Interrupt Type | Priority
DIVIDE ERROR, INT n, INT0 NMI INTR SINGLE STEP | HIGHEST LOWEST

## Slide 24: Thank YOU